RELATIVE SPECTRAL PROCESSING (RASTA):
RASTA is a method of extracting the relevant information from a sound or any audio signal and the main goal of using this technique is to remove the robustness of speech recognition in additive noise or real time environment [1] and it is usually done by using band pass filter of time trajectories of logarithmic value of speech actually it is the extension of original method to the combination of additive noise and convolution noise [2]
Relative spectral processing [RASTA] based speech enhancement involves linear filtering of the trajectory of the short-term power spectrum of noisy speech signal, as shown in Figure. The spectral values of input speech signal are compressed by a nonlinear compression rule (a=2/3) before performing the filtering operation and expanded after filtering (b=3/2) [1].

[1] Deshmukh, Ratnadeep & Kurzekar, Pratik & Waghmare, Dr. Vishal & P. Shrishrimal, Pukhraj. (2014). A Comparative Study of Feature Extraction Techniques for Speech Recognition System. International Journal of Innovative Research in Science, Engineering and Technology. 3. 18006-18016. 10.15680/IJIRSET.2014.0312034.
[2] Hynek Hermansky, and Nelson Morgan, "RASTAA Processing of Speech", IEEE Transactions On Audio, Speech & Language Processing,
Vol 2, No. 4, pp. 578-589, October 1994

     MFCC is one of the most important feature extraction technique that is actually based over the human’s ear scale bandwidth. It uses the low and the high frequencies, measured in Hz to get the speech signal. These signals are then divided into the audio frames to calculate the MFCC. Let each frame consist of N samples and let adjacent frames be separated by M samples where M<N. Each frame is multiplied by a Hamming window where the Hamming window equation is given by:
[12]
Then speech signal is converted to frequency domain from time domain by using its Fourier Transform. The Discrete Fourier Transform (DFT) of a signal is defined by the following:
𝑋𝑘 = 𝑥𝑖𝑒 − 𝑗2𝜋𝑘�[12]
The melfrequency scale is a linear frequency spacing below 1000 Hz and a logarithmic spacing above 1000Hz .As a reference point ,the pitch of a 1 KHz tone ,40dB above the perceptual hearing threshold, is defined as 1000 mels. Therefore we can use the following approximate formula to compute the mels for a given frequency f in Hz.
Mel(f) = 2595*log10(1 + f/700)[13]
The MFCC features are corresponding to the log total energy in a critical band around the center frequency is included. as a final point the Inverse Discrete Fourier Transformer is applied for the cepstral coefficients calculation, finally calculate DCT of the output from the filterbank.
𝑋𝑘 = 𝛼 𝑥𝑖 cos { 2𝑖 + 1 𝜋𝑘 2𝑁 }
The resultant value is the actual Mel-Frequency Cepstral Coefficient.

IS K BAAD EKK FRAMEWORK DIAGRAM HAI IS K FLOW KI